|  |  | Attachment B Project Summary |
| --- | --- | --- |
|  |  | New Stockton Courthouse Superior Court of California County of San Joaquin |

PROJECT DESCRIPTION

The project is the design, construction, and commissioning of a new building and site development for a trial court facility comprised of approximately 325,000 gross square feet.  The CEQA/Environmental Impact Report process is in progress and selection of the site is not final.  Test fits of the project on the two possible sites, the Hunter Square and the Washington Street sites,  are included in Attachment J, Conceptual Design Documents.  The approximately 12 story building with a basement includes but is not limited to all building structure, exterior enclosure, mechanical, electrical, telecommunication, audio visual, and security systems, vertical transportation, holding and detention elements, loading dock equipment, building maintenance equipment, interior improvements, case work, fixtures, furnishings, and equipment, and window treatments.  The site development includes but is not limited to site preparation, demolition of existing structures, underground utilities, landscape, hardscape, vehicular drives, security elements, perimeter fencing, and gates.  The site is to be cleared of site improvements and existing underground utilities. Furnishing and installation of interior furniture, furnishings, and fixtures will be performed under a separate, but concurrent contract.

###### PROJECT GOALS

## This project will be consistent with the California Trial Court Facilities Standards, February 2006, adopted by the Judicial Council of California. The purpose of the standards are to produce high performing public buildings with a positive architectural legacy that reflects the Judicial Council’s commitment to providing equal access to justice.

The specific goals for the project are:

## 1. 	Design – The Courthouse will function equally well as a setting for the delivery of justice, as a public services center, as a community landmark and as a statement of the community’s heritage.

## 2. 	Schedule and Cost – The project design and construction will be completed the within the approved schedule and within the authorized funds. Where possible, project tasks should be concurrent.

## 3. 	Courthouse Life Span – This facility should function effectively for several generations.  The design shall support a logical and cost effective approach to incremental construction without undue disruption of court operations.  The design shall accommodate change over time in court operations.

## 4. 	Design Quality Assurance – Periodic peer review shall be sought throughout the phases of the project for enhanced quality assurance.  The entire project team shall utilize quality assurance procedures to ensure that the contract documents result in change orders issued to the construction contractor of less than 2% of the original contract amount.

## 5. 	Sustainable Design/LEED “Silver” Certification -- The Project shall be designed for sustainability and to the standards of the United State Green Building Council’s (USGBC) LEEDTM “Silver” or better rating.  The project will receive certification by the USGBC as well as participate in the incentives/rewards program sponsored by the local utility company.  The building shall consume 20% less energy or better than a code minimum facility by the use of energy efficient materials, equipment, and systems consistent with the project budget.

## 6. 	Accessibility – Design of building shall reflect Judicial Council’s mission to provide “access to justice” for all, including equal access and fairness with the highest quality of justice and service to the public. The building shall incorporate universal design concepts, to make the facility accessible to all users without treating persons with disabilities differently.

## 7. 	Security – The design will provide for efficient and safe court operations in a cost effective manner. Security measures for the building and site shall meet the requirements of the AOC and County Sheriff.

## 8. 	Durability, Quality and Efficiency – Materials and systems for the building and site should be chosen with regard to the amount of traffic, use and visibility of each space or area.  Materials should be durable, operationally and energy efficient, easily cleaned/maintained, and environmentally friendly.

## 9. 	Commissioning – A total building commissioning program shall be implemented to ensure that the building systems perform interactively in accord with the design intent.

Funding Sources – Funding of this project was approved for the site Acquisition Phase in the 2007-08 State Budget Act and for Preliminary Plans (Schematic Design and Design Development) phases in the 2008-09 State Budget Act. Upcoming state budget requests will be for the Working Drawings phase in fiscal year 2009-2010 and the Construction phase in the fiscal year 2010-2011.

Project Budget – The overall construction budget is approximately $193,262,000 (escalated to reflect costs at mid-point of construction), not including FF&E, construction contingencies, fees for professional services, or other owner “soft” costs”.  The budget amount must not be exceeded.  OCCM is responsible for maintaining individual line items in the budget and for budget modification throughout the project.  See Cost Responsibility Matrix (Attachment I) and Construction Phase Scope Detail (Attachment C) for the scope of work anticipated in the construction contract.

Preliminary Project Program1

| SUMMARY OF SPACE REQUIREMENTS |  | Net Area | Dept. Area | Gross Area |
| --- | --- | --- | --- | --- |
| PRIMARY PROGRAM |  |  |  |  |
| Public Areas: Entry & Security Screening |  | 4,474 | 5,369 | 7,248 |
| Court Sets (30 courtrooms) |  | 83,000 | 99,600 | 134,460 |
| Collaborative Court Staff |  | 2,866 | 3,726 | 5,030 |
| Judicial Chambers & Courtroom Support |  | 13,640 | 17,732 | 23,938 |
| Criminal Division |  | 8,432 | 11,383 | 15,367 |
| Civil Division |  | 6,390 | 8,627 | 11,646 |
| Family Court & Dependency Division |  |  |  |  |
| Family Court Operations |  | 5,994 | 8,092 | 10,924 |
| Family Court Mediation Unit |  | 2,914 | 3,788 | 5,114 |
| Self Help Service Center |  | 2,696 | 3,505 | 4,731 |
| Children’s Waiting Room |  | 460 | 598 | 807 |
| Court Administration |  | 10,367 | 13,271 | 17,916 |
| Court Operations |  | 4,682 | 6,087 | 8,217 |
| Jury Services |  | 9,091 | 10,909 | 14,727 |
| Staff Support |  | 1,424 | 1,709 | 2,307 |
| Related Justice Agency Space |  | 860 | 1,032 | 1,393 |
| Court Security Operation |  | 2,368 | 3,078 | 4,156 |
| In-Custody Holding – Central |  | 5,580 | 8,370 | 11,300 |
| Building Operations |  | 2,670 | 3,204 | 4,325 |
| Sub Total |  | 167,908 | 210,079 | 283,607 |
| SUPPORT PROGRAM |  |  |  |  |
| Judge and Staff Parking |  |  |  | 17,325 |
| Loading |  |  |  | 4,060 |
| Sally Port and Sheriff Parking |  |  |  | 6,750 |
| Building Systems |  |  |  | 20,000 |
| Sub-Total |  |  |  | 48,135 |
| Grand Total without Grand Jury |  |  |  | 331,742 |
| Grand Jury (optional, TBD) |  | 1,270 | 1,651 | 2,229 |
| Grand Total with Grand Jury |  |  |  | 333,971 |
| Building Gross Area |  |  |  | 283,607 |
| Gross Area per Courtroom (30 Courtrooms) |  |  |  | 9,454 |
| Original Program from Feasibility Study |  |  |  | 282,735 |
| Net Change |  |  | 0.31% | 872 |
| Total Number of Staff |  |  |  | 373 |

1	Functional areas subject to change.

2	Component gross square feet (CGSF) are the amount of area required by a department or component for its individual functions including internal circulation.

3	Building gross square feet (BGSF) is the amount of area for the entire enclosed building including general horizontal and vertical circulation; space required for mechanical, electrical, and structural systems.

* * *